## Slide 1
PJT-I
Personalized Adaptive
Posture Correction Belt
End-to-End Technical Pipeline
Technical project review
Current phone / Expo prototype
IMU
Orientation
Filtering
Calibration
Deviation
Stability
Persistence
Feedback
Correction
Adaptation
Session Analytics
Daily / Weekly Analytics
↓
↓
↓
↓
↓
↓
↓
↓
↓
↓
↓
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/master_context.md
/Users/dracon/posture-belt/App.tsx
The cover is a compact conceptual walkthrough, not an execution-order assertion. Adaptive controllers feed the next local sample. Current hardware is the phone prototype.

## Slide 2
System pipeline overview
Local posture decisions, session-local adaptation and asynchronous history
2
REAL-TIME DEVICE PATH
Raw IMU
Orientation
+ filter
Body
mapping
Calibrated
reference
Deviation
Stability
Persistence
Feedback
LOCAL ADAPTATION
Completed corrections
Response history → adaptive feedback → eligible haptics
Posture + corrections → features / EMA → next threshold
ASYNCHRONOUS COMPLETED-SESSION PATH
Session + metrics
Express / SQLite
Session detail or Daily / Weekly
Adaptive threshold feeds future deviation checks. Backend/database is outside the real-time loop.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/App.tsx
/Users/dracon/posture-belt/master_context.md

## Slide 3
Raw IMU acquisition
Acceleration and angular velocity provide the sensor inputs
3
ACCELEROMETER
aₓ, aᵧ, az
GYROSCOPE
gₓ, gᵧ, gz [rad/s]
≈ 50 Hz target Δt ≈ 20 ms
Accelerometer callback → Latest cached gyro + Date.now() → Timestamped sample
ASSUMPTION / CONSTRAINT
Consistent mounting. Callback cadence varies with the device.
Raw IMU values are measurements, not direct posture angles.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/services/imuService.ts
/Users/dracon/posture-belt/App.tsx

## Slide 4
Accelerometer orientation
Gravity provides the long-term orientation reference
4
P(acc) = atan2(−aₓ, √(aᵧ² + az²)) × 180/π
R(acc) = atan2(aᵧ, az) × 180/π
Acceleration vector → Gravity-based angle estimate → Sensor pitch / roll in degrees
ASSUMPTION / CONSTRAINT
Gravity must dominate the long-term signal. Linear acceleration disturbs it.
Accelerometer orientation anchors the filter over time.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/orientation.ts

## Slide 5
Gyroscope integration
Angular velocity gives the fast orientation-change estimate
5
P(gyro) = P(previous) + gᵧ × Δt × 180/π
R(gyro) = R(previous) + gₓ × Δt × 180/π
Gyro [rad/s] + elapsed seconds → Integration → Short-term sensor angles
ASSUMPTION / CONSTRAINT
App accepts 0 < Δt ≤ 1 s. The first filtered state uses accelerometer angles.
Gyroscope responds quickly, but integration accumulates drift.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/orientation.ts
/Users/dracon/posture-belt/App.tsx
dt is (timestamp-lastTimestamp)/1000. Invalid intervals rebase lastTimestamp and return. gz is acquired but not used for pitch/roll.

## Slide 6
Complementary filter
Fuse fast gyro response with a long-term gravity reference
6
Angle(t) = 0.98 × Angle(gyro) + 0.02 × Angle(acc)
Gyro angle + accelerometer angle → Weighted fusion → Filtered sensor pitch / roll
ASSUMPTION / CONSTRAINT
α = 0.98 is the implemented fixed filter coefficient.
Short-term responsiveness and long-term reference coexist.
Gyroscope 98%
Accelerometer 2%
Fused orientation
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/orientation.ts

## Slide 7
Sensor-to-body frame mapping
Convert phone orientation into meaningful posture coordinates
7
BodyPitch = 90° − SensorRoll
BodyRoll = SensorPitch
Filtered sensor angles → Fixed frame mapping → Body pitch / roll
ASSUMPTION / CONSTRAINT
Current mounting is portrait and fixed. Belt mounting needs physical verification.
The same body-frame convention governs calibration and correction.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/orientation.ts
/Users/dracon/posture-belt/master_context.md

## Slide 8
Personalized calibration
Learn the user’s natural comfortable upright reference
8
μₚ = (Σ Pᵢ) / n μᵣ = (Σ Rᵢ) / n
σ = √[ Σ(xᵢ − μ)² / n ]
Natural upright samples → Mean + population standard deviation → Canonical posture model
ASSUMPTION / CONSTRAINT
Current collection: 30 s. Intended engineering range: 30–60 s.
Calibration learns a personal reference rather than universal zero.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/calibration.ts
/Users/dracon/posture-belt/App.tsx
Confidence = mean(max(0,1-pitchStd/4),max(0,1-rollStd/4))*100. It is an engineering variability indicator, not clinical certainty.

## Slide 9
Calibration validity and storage
Validated canonical calibration survives application restart
9
n ≥ 100 σₚ ≤ 4° σᵣ ≤ 4°
Valid calibration
Versioned
AsyncStorage
Load + validate
Calibrated idle
Explicit recalibration → Replace saved canonical model → New baseline
ASSUMPTION / CONSTRAINT
No recalibration during monitoring or unresolved upload. Invalid storage requires calibration.
Canonical calibration remains separate from session-local adaptive state.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/calibration.ts
/Users/dracon/posture-belt/services/calibrationStorage.ts
/Users/dracon/posture-belt/services/calibrationStorageModel.ts
/Users/dracon/posture-belt/App.tsx

## Slide 10
Personalized deviation
Evaluate current posture relative to canonical baselines
10
Dₚ = |P − μₚ| Dᵣ = |R − μᵣ|
PitchOutside = Dₚ > Tₚ RollOutside = Dᵣ > Tᵣ
Body posture + baseline → Absolute deviation + threshold test → Outside flags
ASSUMPTION / CONSTRAINT
Overall deviation = PitchOutside OR RollOutside. Equality remains inside.
The personalized reference stays fixed while effective tolerance can vary.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/deviation.ts

## Slide 11
Canonical personalized threshold
Combine minimum tolerance with each axis’s natural variability
11
Tₚ(canonical) = 4° + 2σₚ
Tᵣ(canonical) = 4° + 2σᵣ
Calibration variability → Minimum tolerance + variability term → Canonical thresholds
ASSUMPTION / CONSTRAINT
4° minimum and factor 2 are engineering parameters, not medical cutoffs.
Monitoring never rewrites the canonical thresholds.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/deviation.ts
/Users/dracon/posture-belt/App.tsx

## Slide 12
Dominant posture direction
Magnitude selects the axis, signed baseline difference selects direction
12
Dₚ ≥ Dᵣ → pitch axis
otherwise → roll axis
+ pitch: Forward − pitch: Backward
+ roll: Right − roll: Left
Deviation magnitudes + signed offset → Dominant-axis selection → Direction label
ASSUMPTION / CONSTRAINT
Positive/negative means relative to the calibrated baseline. Pitch wins ties.
Direction preserves the specific axis that generated the alert.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/App.tsx
/Users/dracon/posture-belt/models/postureModel.ts

## Slide 13
Stability detection
Test variability in a rolling two-second window
13
σₚ(window) ≤ 2° AND σᵣ(window) ≤ 2°
window ≤ 2 s minimum n = 10
Body pitch / roll history → Window variability → Stable / unstable
ASSUMPTION / CONSTRAINT
The detector needs 10 samples, not necessarily a full two seconds of history.
Stability rejects dynamic movement before persistence can accumulate.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/stability.ts
/Users/dracon/posture-belt/App.tsx

## Slide 14
Persistence detection
Require sustained deviation while posture remains stable
14
Outside threshold
Stable
Elapsed ≥ 3 s
Feedback eligible
Accumulate only when: deviation AND stable
Stable outside state → Timestamp-based persistence → Sustained flag
ASSUMPTION / CONSTRAINT
Losing deviation or stability resets persistence immediately.
A transient deviation cannot trigger feedback on its own.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/persistence.ts
/Users/dracon/posture-belt/App.tsx

## Slide 15
Layered false-feedback suppression
Each stage addresses a different source of unwanted alerts
15
Raw sensor
noise
Complementary
filter
Personalized
threshold
Stability
Persistence
Feedback
Fusion: orientation noise and gyro drift
Personalization: natural individual variation
Stability + persistence: dynamic or brief deviations
ASSUMPTION / CONSTRAINT
No extra smoothing or feedback cooldown is implemented.
Layered decisions separate sensor variation from sustained deviation.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/orientation.ts
/Users/dracon/posture-belt/processing/deviation.ts
/Users/dracon/posture-belt/processing/stability.ts
/Users/dracon/posture-belt/processing/persistence.ts
/Users/dracon/posture-belt/App.tsx

## Slide 16
Feedback controller
Translate sustained deviation and current feedback mode into a command
16
shouldVibrate = sustainedDeviation
Stateless decision layer
Start observation only when no correction is active
One real feedback event per new observation
Persistence + adaptive feedback mode → Eligibility → Haptic command
ASSUMPTION / CONSTRAINT
Adaptive mode cannot bypass stability or persistence. No feedback cooldown.
Feedback eligibility and command reassertion are separate decisions.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/feedback.ts
/Users/dracon/posture-belt/App.tsx
/Users/dracon/posture-belt/processing/adaptiveFeedback.ts

## Slide 17
Phone haptic feedback
Repeat the current vibration command until target-axis correction
17
Vibration.vibrate([0, 200, 100], true)
0 ms delay 200 ms on 100 ms off repeat
Eligible feedback → Continuous repeating phone pattern → Tactile prompt
ASSUMPTION / CONSTRAINT
Fixed vibration behavior. Variable amplitude/intensity is NOT implemented.
Correction or lifecycle stop calls Vibration.cancel().
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/services/hapticService.ts
/Users/dracon/posture-belt/App.tsx

## Slide 18
Correction response tracking
Measure return within the alerted axis’s effective threshold
18
T(response) [s] = (t(correction) − t(feedback)) / 1000
WAITING → OBSERVING → CORRECTED
Feedback + target-axis outside flag → Observe until target returns inside → Completed response
ASSUMPTION / CONSTRAINT
Forward/backward checks pitch. Left/right checks roll. No timeout failure state.
The unrelated axis can remain outside when the target correction completes.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/correctionResponse.ts
/Users/dracon/posture-belt/App.tsx
Timestamps are milliseconds. ResponseTime is seconds. The result is frozen until a new observation/reset. App records initial/final max-axis deviation, direction, timestamps and response time exactly once.

## Slide 19
Adaptive feedback response history
Classify only completed corrections from the current session
19
T < 3 s FAST
3 s ≤ T ≤ 6 s NORMAL
T > 6 s SLOW
Completed response times → Bounded latest-five history → Feedback mode evidence
ASSUMPTION / CONSTRAINT
Ignore incomplete/non-finite responses. Reset history for each new session.
Slow correction describes response behavior, not physiological fatigue.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/adaptiveFeedback.ts

## Slide 20
Adaptive feedback modes
Modes vary command persistence without varying vibration amplitude
20
NORMAL
No consistent slow pattern
Start once, no reassertion timer
PERSISTENT
≥ 2 slow among latest 3 responses
Reassert the same command every 6 s
HIGH_PERSISTENCE
≥ 4 slow among latest 5 responses
Reassert the same command every 3 s
ASSUMPTION / CONSTRAINT
Timer requires active monitoring AND active correction observation.
Correction always stops reassertion and vibration.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/adaptiveFeedback.ts
/Users/dracon/posture-belt/App.tsx

## Slide 21
Purpose of adaptive thresholds
Account for behavioral evidence consistent with prolonged-use difficulty
21
Canonical
tolerance
Changing
behavior
Multiple
features
Bounded effective
threshold
Evidence develops from observed trends within one session
Posture + completed corrections → Behavioral evidence → Temporary axis-specific adjustment
ASSUMPTION / CONSTRAINT
No physiological fatigue detection, learned model or backend-driven adaptation.
Adaptive tolerance leaves the natural-posture reference unchanged.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/adaptiveThreshold.ts
/Users/dracon/posture-belt/processing/adaptiveThresholdFeatures.ts
/Users/dracon/posture-belt/master_context.md

## Slide 22
Five normalized adaptive features
Pitch and roll maintain independent posture-feature state
22
f₁ Deviation trend
f₂ Deviation frequency trend
f₃ Completed correction-response trend
f₄ Declining good-posture period duration
f₅ Increasing near-threshold exposure
fᵢ ∈ [0, 1]
Near threshold
75–100% of T
ASSUMPTION / CONSTRAINT
Correction trend is shared session context. Near-threshold exposure alone is not bad posture.
Multiple trends contribute evidence without reconstructing physiological state.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/adaptiveThresholdFeatures.ts
/Users/dracon/posture-belt/processing/adaptiveThreshold.ts

## Slide 23
Equal-weight behavioral evidence
Combine the implemented normalized features without learned weights
23
Eₜ = (f₁ + f₂ + f₃ + f₄ + f₅) / 5
0 ≤ Eₜ ≤ 1
Five normalized features → Arithmetic mean → Per-axis combined evidence
ASSUMPTION / CONSTRAINT
No sufficiently labelled dataset or validated learning reward supports learned weights.
Each behavioral feature contributes one fifth of the evidence.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/adaptiveThresholdFeatures.ts
/Users/dracon/posture-belt/master_context.md

## Slide 24
Timestamp-aware temporal adaptation
Smooth feature trends and combined evidence using elapsed time
24
EMAₜ = αXₜ + (1 − α)EMA(previous)
α = 1 − exp(−Δt / τ)
Timestamped features / evidence → Short, long and evidence EMAs → Smoothed behavioral state
ASSUMPTION / CONSTRAINT
DEMO τ: short 5 s, long 30 s, evidence 15 s. Production: 2 min, 10 min, 10 min.
EMA updates use actual elapsed time, not an assumed sample rate.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/adaptiveThresholdFeatures.ts
/Users/dracon/posture-belt/processing/adaptiveThresholdConfig.ts
All time units in alpha are consistent (milliseconds). First valid EMA sample initializes its value. Non-increasing timestamps retain the prior value. DEMO is accelerated and not final production tuning.

## Slide 25
Adaptive safety gates
Allow threshold movement only after evidence and safety checks pass
25
Enough data?
Stable?
No severe
deviation?
No major
deterioration?
Allow movement
DEMO data gate
≥ 20 s observed and ≥ 100 valid processed samples
≥ 3 completed corrections and ≥ 2 good periods per axis
ASSUMPTION / CONSTRAINT
Major deterioration: deviation trend ≥ 0.75 AND frequency trend ≥ 0.75.
Any failed gate freezes that axis’s current adjustment.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/adaptiveThreshold.ts
/Users/dracon/posture-belt/processing/adaptiveThresholdConfig.ts

## Slide 26
Bounded adaptive threshold adjustment
Add a temporary non-negative tolerance to each canonical threshold
26
T(effective) = T(canonical) + A
0° ≤ A ≤ 3°
Canonical threshold + evidence state → Safety-gated bounded adjustment → Next effective threshold
ASSUMPTION / CONSTRAINT
DEMO rate ≤ 1.5°/min, elapsed step ≤ 5 s. Production ≤ 0.25°/min, step ≤ 60 s.
Each new session starts with zero pitch and roll adjustment.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/adaptiveThreshold.ts
/Users/dracon/posture-belt/processing/adaptiveThresholdConfig.ts
/Users/dracon/posture-belt/App.tsx
Target=3*clamp01((evidenceEma-0.30)/(1-0.30)). Rate limit moves current toward target. The App classifies with the current adjustments before updating the controller, so new state applies to a subsequent sample.

## Slide 27
Recovery toward canonical thresholds
Decreasing evidence lowers the permitted adjustment target
27
A(target) = 3° × clamp₀₋₁[(EMA(E) − 0.30) / 0.70]
Evidence decreases
Target decreases
Rate-limited recovery
T_effective approaches
T_canonical
Lower evidence EMA → Move adjustment toward target → Reversible tolerance
ASSUMPTION / CONSTRAINT
Recovery also requires passing safety gates. A veto freezes current state.
Temporary relaxation never becomes a replacement baseline.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/adaptiveThreshold.ts
/Users/dracon/posture-belt/processing/adaptiveThresholdConfig.ts

## Slide 28
Severe-deviation veto
High evidence cannot override severe current posture deviation
28
D(axis) > 2 × T(axis, effective) ⇒ freeze A(axis)
Current axis deviation + effective threshold → Severe-deviation check → No further relaxation
ASSUMPTION / CONSTRAINT
The veto is per axis and holds its existing adjustment. It does not reset calibration.
Safety takes precedence over the behavioral evidence score.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/adaptiveThreshold.ts
/Users/dracon/posture-belt/test/adaptiveThreshold.test.mjs

## Slide 29
Traceable session recording
Record the exact posture values and events used by the running system
29
SESSION
id + start/end + duration + sampling
canonical calibration snapshot
samples[] + feedbackEvents[]
completed correctionResponses[]
POSTURE SAMPLE
timestamp, body pitch / roll
absolute deviations
effective thresholds
acceptability + direction
ASSUMPTION / CONSTRAINT
Start time is the first valid monitoring sample. Events/responses reject duplicates.
Recording preserves evidence for later session analysis.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/sessionRecorder.ts
/Users/dracon/posture-belt/App.tsx
Session has no nested metrics field. SessionUpload adds metrics when sending the completed object. Stored sample overallDeviation is a numeric maximum of axis deviation, unlike the detector Boolean of the same name.

## Slide 30
Session performance metrics
Compute existing metrics only after session finalization
30
Consistency = GoodPostureTime / MonitoredDuration × 100
CompletionRate = CompletedCorrections / FeedbackEvents × 100
MeanCorrectionTime = (Σ responseTimeᵢ) / N_completed
Finalized samples + feedback + responses → Existing metric calculator → Session metric snapshot
ASSUMPTION / CONSTRAINT
No responses: correction mean is null. Zero denominators: core metrics return 0.
Completion rate measures recorded response behavior, not clinical success.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/performanceMetrics.ts

## Slide 31
Observed posture time and sampling
Preserve measured timing rather than assuming perfect 50 Hz delivery
31
GoodTime = Σ positive Δtᵢ where sampleᵢ is acceptable
ActualRate = SampleCount / (MonitoredDuration / 1000)
Adjacent sample timestamps → Earlier-sample interval convention → Recorded good time + Hz
ASSUMPTION / CONSTRAINT
The last-sample-to-stop tail remains unclassified. Duration fields are milliseconds.
Poor time needs raw intervals and cannot equal total time minus good time.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/processing/performanceMetrics.ts
/Users/dracon/posture-belt/processing/sessionRecorder.ts
/Users/dracon/posture-belt/ui/sessionAnalytics.ts
/Users/dracon/posture-belt/ui/historyGrouping.ts

## Slide 32
Completed-session lifecycle
Finalize locally before asynchronous upload or historical refresh
32
Stop monitoring
Cancel feedback
Finalize once
Calculate metrics
Upload asynchronously
Results remain visible while uploading
Failure retains the same session and ID for manual retry
HTTP 409 means possibly saved, not confirmed persistence
ASSUMPTION / CONSTRAINT
Pending uploads live in memory only. No durable offline queue or automatic retry.
Network availability never decides real-time posture feedback.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/App.tsx
/Users/dracon/posture-belt/services/apiService.ts

## Slide 33
Backend session persistence
Express validates completed-session JSON before SQLite storage
33
POST /api/sessions
Runtime validation
SQLite WAL
Stored session JSON
Valid upload → 2xx Malformed / non-finite → 400
Duplicate session ID → 409
GET /api/sessions/:id retrieves one full stored session
ASSUMPTION / CONSTRAINT
50 MB JSON limit. backend/posture.db is host-local runtime data.
Backend storage stays outside the sensor-to-feedback loop.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/backend/src/server.ts
/Users/dracon/posture-belt/backend/src/routes/sessions.ts
/Users/dracon/posture-belt/backend/src/database.ts
/Users/dracon/posture-belt/services/apiService.ts

## Slide 34
Historical metrics API
Derive aggregate summaries and compact trends from persisted sessions
34
GET /api/metrics/summary
All-time weighted totals + coverage counts
GET /api/metrics/trends
Chronological per-session metrics, without raw samples
ASSUMPTION / CONSTRAINT
Legacy/incompatible rows are excluded and counted. No historical adaptive evidence.
Weekly and Daily aggregate trend records without fetching all raw sessions.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/backend/src/analytics.ts
/Users/dracon/posture-belt/backend/src/routes/metrics.ts

## Slide 35
Individual-session analytics
One session answers what happened at sample and event level
35
Posture timeline + pitch / roll deviation
Deviation distribution + directional feedback
Completed responses + directional correction times
Recorded effective thresholds + derived adjustments
Stability history and adaptive evidence history: UNAVAILABLE
ASSUMPTION / CONSTRAINT
Stored samples support threshold history, not controller evidence or veto history.
The full Session dashboard opens from an explicit session selection.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/ui/sessionAnalytics.ts
/Users/dracon/posture-belt/components/SessionResultsDashboard.tsx
/Users/dracon/posture-belt/master_context.md

## Slide 36
Daily historical analytics
Aggregate all sessions whose start date belongs to one selected local day
36
DailyConsistency = Σ GoodTime / Σ MonitoredTime × 100
Session trends + whole-day direction / valid time-of-day usage
Selected-day sessions → Duration-weighted aggregation → Complete day report
ASSUMPTION / CONSTRAINT
Chart points are sessions. Cross-midnight sessions belong to their start date.
Daily reports usage, posture and response behavior across the whole day.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/ui/historyGrouping.ts
/Users/dracon/posture-belt/components/HistoricalAnalyticsDashboard.tsx
Daily charts show session consistency,duration,feedback,completed corrections,mean response. Direction and time-of-day usage summarize the whole day. Chart pages have six sessions but aggregate totals include every session. Poor duration is unavailable from trend records.

## Slide 37
Weekly historical analytics
Aggregate all selected-week sessions, with days as chart points
37
WeeklyConsistency = Σ GoodTime / Σ MonitoredTime × 100
Daily consistency, duration, feedback, corrections and response time
Monday–Sunday local calendar → Seven daily aggregates → Complete week report
ASSUMPTION / CONSTRAINT
Missing days are N/A, never measured 0%. Daily average usage = week total / 7.
Weekly shows how recorded daily usage and response metrics vary.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/ui/historyGrouping.ts
/Users/dracon/posture-belt/components/HistoricalAnalyticsDashboard.tsx
Charts: daily consistency,duration,feedback,completed corrections,mean correction time,good-time/poor-unavailable chart and weekly direction. Poor time is explicitly unavailable. Correction average weights session means by completed correction count.

## Slide 38
Duration-weighted consistency
Illustrative arithmetic example, not a measured project result
38
Session A: 10 min at 90% Session B: 100 min at 60%
Simple mean: (90 + 60) / 2 = 75%
Time-weighted: (9 + 60) / 110 × 100 = 62.7%
ASSUMPTION / CONSTRAINT
Aggregate recorded good time and monitored time, not session percentages.
Longer monitoring periods contribute proportionally more.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/ui/historyGrouping.ts
/Users/dracon/posture-belt/backend/src/analytics.ts
Illustrative example requested by the user. Session A: 10min at90%=9min good. B:100min at60%=60min good. Total69/110=62.727%. These are not collected measurements.

## Slide 39
Session, Daily and Weekly ownership
Different analytical units answer different engineering questions
39
SESSION
DAILY
WEEKLY
Samples / events
Sessions
Calendar days
What happened?
How was the day?
How was the week?
ASSUMPTION / CONSTRAINT
All period totals include every compatible dated session in the selected period.
Historical aggregation preserves the existing session metric definitions.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/master_context.md
/Users/dracon/posture-belt/ui/historyGrouping.ts
/Users/dracon/posture-belt/ui/sessionAnalytics.ts

## Slide 40
Validation boundary and hardware roadmap
Engineering/software validation does not establish physical or clinical performance
40
SOFTWARE-VALIDATED
Deterministic processing and safety gates
Lifecycle, persistence and analytics
TypeScript and Android export
PHYSICAL VALIDATION PENDING
IMU cadence and mounting signs
On-body calibration and response
Wearable haptic perception
Future belt: MCU → suitable driver → actuator
ASSUMPTION / CONSTRAINT
Current adaptive timing is DEMO/accelerated. Hardware intensity needs experimental calibration.
No ML prediction, physiological fatigue, clinical benefit or amplitude adaptation claim.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/docs/final_validation_matrix_and_hardware_protocol.md
/Users/dracon/posture-belt/master_context.md
/Users/dracon/posture-belt/test/adaptiveSystemEvaluation.test.mjs
/Users/dracon/posture-belt/test/historyAnalytics.test.mjs

## Slide 41
Complete end-to-end technical reference
Local sensing and adaptation produce traceable completed-session history
41
REAL-TIME
IMU
Orientation
Filter
Body mapping
Calibrated
reference
Deviation
Stability
Persistence
Haptics
ADAPTIVE
Completed corrections
Response history → adaptive feedback → eligible haptics
Posture + corrections → features / EMA / gates → next threshold
SESSION / HISTORICAL
Record + metrics
Async API / SQLite
Session detail or Daily / Weekly
Canonical reference stays fixed. Correction stops feedback. Backend latency stays out of the loop.
Notes: Source snapshot: ff437ef, inspected 5 October 2026.
/Users/dracon/posture-belt/App.tsx
/Users/dracon/posture-belt/master_context.md
/Users/dracon/posture-belt/ui/historyGrouping.ts
This is a conceptual overview of data dependencies. Adaptive feedback and adaptive threshold are independent branches, not a serial feed-forward chain. Session recording runs alongside live processing. The backend summary aggregates JSON. Daily and Weekly use compact trends locally.